## Slide 1
Capacitance IN Series and Parallel
Capacitors IN Series and Parallel
Capacitors are manufactured with certain standard capacitances
Is there a way to obtain specific value of capacitance

## Slide 2
Capacitance IN Series
C1
C2
a
b
Vab=V
+ + + +
+ + + +
- - - -
+Q
-Q
+Q
-Q
c
Vac=V1
Vcb=V2
- - - -

## Slide 3
The combination can be replaced by a equivalent capacitance Ceq
Note: Magnitude of charge on each capacitor is the same, however potential difference can be different
V=V1+V2+V3+ …
Ceq
- - - -
+Q
-Q
+ + + +
V
In general for any number of capacitors in Series

## Slide 4
Capacitance IN Parallel
a
b
+ + + +
- - - -
+ + + +
- - - -
C1
Q1
C2
Q2
Vab=V
The charges are
Ceq
- - - -
Q=Q1+Q2
+ + + +
In general for any number of capacitors in parallel

## Slide 5
Intuitive understanding
Using the plate capacitor formula we derive the equivalent capacitance intuitively
Parallel plate capacitor
Two identical plate capacitors in series means effectively increasing the d
+Q
-Q
+Q
-Q
equipotential
d
d
+Q
d
-Q
d

## Slide 6
Two identical plate capacitors in parallel means effectively
increasing A in
Intuitive understanding
equipotential
+Q
-Q
+Q
-Q
d
d
A
A
+Q
-Q
d
+Q
-Q
d
A
A

## Slide 7: Clicker Question
Ctotal = C/2
1/Ctotal = 1/C + 1/C
= 2/C
Ctotal = C
Ctotal = 2C
C
C
C
C
C
The three configurations shown below are constructed using identical capacitors. Which of these configurations has lowest total capacitance?
A
B
C

## Slide 8
Example
V
C3
C2
C1
(a)Determine the equivalent capacitance of the circuit shown if C1 = C2 = 2C3 = 12.5 F.
(b) How much charge is stored on each capacitor when V = 45.0 V?
Middle Branch: 1/Ceq = 1/C2 + 1/C3  1/Ceq = 1/12.5 F + 1/6.25 F  Ceq = 4.16667 F
Voltage over each parallel branch is same as the battery:
C1: 45.0 V Q1=C1V= 12.5 F 45V= 562.5μC
Ceq: 45.0 V
Combine parallel: C = C1 + Ceq  C = 12.5 F + 4.1666667 F = 16.6667 F
Series: V=V2 + V3 = q/C2 + q/C3 = q/Ceq  q = CeqV  q = (4.166667 F)(45V)= 187.5μC
C2: V = q/C = 187.5 μ C/12.5 F = 15 V
C3: V = 187.5 μ C/6.25 F = 30 V
Check result: V=V2 + V3=15V+30V=45V

## Slide 9
Energy storage in Capacitors
-Q
+Q
Va
Vb
V=Va-Vb
At an intermediate time (t<tcharged)
q is the charge
v is the potential difference
Work dW required to transfer an additional charge dq
The total work W required to increase capacitor charge from 0 to Q
We define potential energy of an uncharged capacitor to be zero then W is equal to potential energy U
Notes: W is the work done by E on Q. q decreases from a initial value Q to 0 as elements of charge dq fall through potential difference v that vary from V to 0

## Slide 10
Electric field energy
We derived the various forms of electric potential energy stored in a capacitor
If we think about charging a capacitor by
moving charge from one plate to the
other that requires work against the electric field
We can think of the energy being stored in the electric field
With
we can introduce the energy density
Using the parallel plate capacitor expressions
and
energy density
Vacuum is not truly
empty space but
can have energy